## Slide 1: Silver Oak College Of Engineering & Technology.
Prepared By:
PAREKH PRATIKKUMAR (29)
JATIN DAVE (45)
SHAH PEARL NEELAMKUMAR (58)
Guided By: Prof. Hasumati Patel

## Slide 2: STONE
Stone: A natural engineering material mainly derived from rocks.
They are available in variety of colors, form and structures.
Stones are strong, durable and descent in appearance.

## Slide 3: Classification on Stones
Mainly classified in 3 ways..
  1) Geological Classification
    Igneous Rocks
    Sedimentary Rocks
    Metamorphic Rocks
    2) Physical Classification
    Stratified Rocks
    Unstratified Rocks
    Foliated Rocks

## Slide 4
    3) Chemical Classification
    Siliceous Rocks
    Argillaceous Rocks
    Calcareous Rocks

## Slide 5: Uses of stone
STONES ARE USED FOR,
Foundations, columns, walls, lintels, arches, floors, damp proof courses, sills etc..
Heavy engg. Works i.e. Dams, Docks, Bridges, Piers, retaining walls, abutments, lighthouses etc..
Paving of roads, footpaths etc..
Railways tracks as ballast.

## Slide 6: Required Properties of Good Stone
Structure
Texture
Strength
Hardness
Durability
Water Absorption
Specific Gravity
Resistance to fire
Facility of dressing
Appearance and color

## Slide 7: BUILDING MATERIAL: BRICKS

## Slide 8: BRICKS
Composition:
Material | Amount of composition
Alumina | 20-30 %
Silica | 50-60%
Lime | 4-6%
Iron Oxides | 4-6%
Magnesium | A small Quantity

## Slide 9: Types of Bricks
Traditional Bricks:
Size:: 23 cm * 11.4 cm * 7.6 cm
Modular Bricks:
  Size :: 19 cm * 9 cm * 9 cm

## Slide 10: Classification of Bricks
First Class Bricks : Used for Superior work of permanent nature
Second Class Bricks : Used for making ballast
Third Class Bricks : Used for inferior and unimportant works
Fourth Class Bricks : Used as aggregate for concrete in foundations, floors, roads etc..

## Slide 11: Qualities of Good Brick
Bricks should have,
  Regular size and shape,
  Uniform and brick-red color,
  Low thermal conductivity,
  Good strength,
  Enough hardness,
  Sound proof,
  Metallic ringing sound when two bricks are struck together..

## Slide 12
BUILDING MATERIAL :
LIME

## Slide 13: LIME
Important cementing material used in engineering construction.
It is the material which has the capacity of holding structural units (like bricks, stones, aggregate) together with sufficient strength.
Classification of lime is,
  Fat Lime,
  Hydraulic lime,
  Poor lime.

## Slide 14: Properties of lime
Fat Lime,
  Hardens very slowly,
  Slakes vigorously,
  Has a high degree of plasticity,
  Has perfectly white color.
  Hardens in combination with air,

## Slide 15
  Hydraulic lime,
  Hardens in combination with water,
  Contains 5-30 % of water,
  Does not shrink much,
  Is not perfectly white colored,
  Forms a thin paste with water,
  Slakes very slowly.
Poor lime,
  Contains more than 30% of clay,
  Slakes and sets very slowly.

## Slide 16: USES OF LIME
Whitewashing and plastering of walls,
Preparation of mortar for thick walls, damp places etc.,
Construction under water,
First class brick and stone masonry works,
For inferior works,
Production of good mortar.

## Slide 17: BUILDING MATERIAL : BITUMEN

## Slide 18: BITUMEN
The Bitumen is a binding material which is present in asphalt.
It is black in color and obtained in solid/semi solid state.
Bituminous materials are very commonly used in highway construction and pavements.

## Slide 19: Classification of Bitumen
Asphalt,
Tar,
Cut-back,
Emulsion.

## Slide 20
Functions of Bituminous Materials
Binding Effect,
Cushion,
Sealing of surface,
Resistance to weathering agents.